High Power Polarized Positron Source

Alexander Mikhailichenko

Cornell U., Ithaca NY 14853

Abstract.  We discuss the basics of polarized positron production by low energy polarized electrons. Efficiency of conversion ~0.1-1% might be interesting for the Continuous Electron Beam Accelerator Facility (CEBAF) and the International Linear Collider (ILC).

Keywords: Positrons, Accelerators, Linac

PACS:52.59-f,  41.75.Ht

1. OVERVIEW

Positrons may be created either by Beta-decay or by the interaction of gammas in field of nuclei. The creation of an e+/e- pair by photons is described in References [1] and [2]. Polarized gammas, suitable for polarized positron production in practical amounts, may be created in three ways: (a) radiation in helical field arranged with help of EM wave, radiation in static field of helical undulator and by radiation due to channeling in helical crystal [3], (b) by scattering laser compton scattering [4], or (c) by Bremstrahlung of initial electron having longitudinal polarization [5]. Process (c) is recomended for CEBAF.   Although generating polarized positrons using a helical undulator K<1, L~150m, λu =1cm (a) is is possible at the ILC we mention the possibility to using method (c) for ILC [14].

2. EFFICIENCY OF POSITRON PRODUCTION

Polarized positron production is a two-stage process. At the first stage, circularly polarized electrons generate longitudinally polarized gammas. At the second stage, these gammas are converted into longitudinally polarized positrons while in the same media as the polarized electron in stage one.  Positrons have more longitudinal polarization at higher energies allowing a polarization enhanced by selecting positrons according to their energy. This procedure is compatible with limiting the energy acceptance of CEBAF SRF structure.

A polarized electron source, a high power target, and a beam collection system are the three main components of a positron source which are the focus of optimization for CEBAF.  The CEBAF polarized source delivers up to 60 MeV of at least 7-% polarized electrons at currents of approximately 100 μA at present plans to deliver 200 μA ,DULY R Inc [12]).  The ILC source has a beam current of ~48 μA.

Radiation protection and shielding is last but not least in this positron source design. Neutron photo-production has a threshold that depends on the target material. For Tungsten, gammas with an energy E< 6.19 MeV can not generate neutrons [7,8] and for the reaction (, 2n) the threshold is 13.6 MeV (W). The threshold for other materials may be found in Reference 11 and the references therein.  Unfortunately, using electrons having energy below this threshold is not preferred as the efficiency of positron production by gammas at 5 MeV compared with 50 MeV drops at least 10 fold plus the efficiency of creating gammas drops by ~i.e. 100 fold. One can find calculations of efficiency for 50 MeV electrons in [5]. The total number of positron created by each electron finally comes to [5]

(1)

where  , thickness of target d measured in units of radiation length (r.l.) X0. Polarization may be approximated as  [1]. Emittance of the beam is ~0.084 [10].

For example:  When positrons are collected within a 25% energy interval around maximal energy, 0.25, and the target thickness is d=0.3, then the efficiency () is1.5%.   The degree of polarization

An efficiency of ~1% requires that the electron current must be at least 100 times bigger than the desired positron current. The positron collection efficiency will also constrain the maximum deliverable positron current.  For narrow energy interval, the collection efficiency could be ~20% and result in a net electron to positron current ratio (Ielectron/Ipositron) of ~500. A desired positron current of 1 microAmpere would require an incident electron current of at 0.5 mA.

A 0.3 r.l. target corresponds to a thickness of ~0.12cm for tungsten or lead; Titanium would not be desireable.  The energy deposited in a 0.3 r.l. target is 2MeV/(g/cm2) x0.3x6.8g/cm2 =4.1MeV. This yields the power deposition in a target ~0.5mAx4MeV~2 kW.  A positron current of 0.1 µA would need a target capable of dissipating 0.5 kW.  The effective depth at which positrons are created is .

HIGH POWER TARGETS

High power targets could be subdivided into two classes: rotating targets and liquid metal ones.  The goal of a high power target is to distribute the deposited energy in the largest volume of material as possible without depleting positron production efficiency.

Liquid Metal Target

Below are the estimated properties of several different liquid lead target candidates.

Pb/Bi:

Liquid at Tl=125.9oC, boiling phase at Tb=~1500oC, latent heat =860 kJ/kg, r~10g/cm3. 83Bi-82Pb alloy composed with 55.51Mass% of Bi and 44.49 Mass% of Pb. Other alloy, Pb-Sn, composed by 61.9 % of Sn has liquid phase at ~183 oC –advantage of Bi-Pb is obvious.

Mercury:

Z=80, liquid at Tl=-38.87oC, boiling at Tb=~357oC. Latent heat =294 kJ/kg, r~13.54 g/cm3 . One negative property of Mercury, what may strictly influence the choice – is its toxicity. Hg is considered one of most toxic materials; however it could be handled properly. In some installations the Mercury is in use in the turbine circle, instead of water which is what gives assurance of success of its implementation for the purposes of positron production. Usage of Hg as a proton target described in [17].

(a)                                                                   (b)

Figure 1. To avoid damage we suggested that liquid metal jet hits the free liquid metal surface (a) ; isometric view on the target, (b).

Let the jet transverse size be 2mm, size along the beam -1.2mm, velocity of jet=10m/sec  so in 1 second the volume of material flowing through the nozzle comes to V≈2.4x104 mm3=2.4x10-2 dm3. For average power deposition 5kW (Q=5 kJ per second) the temperature rise of this amount of material comes to

It begins vaporizing, so the latent heat of vaporization needs to taken into account, and it will take ΔQ ≈860x0.024x10=206 kJ  for Bi-Pb and ΔQ ≈ 95kJ for Hg. So Bi-Pb will remain at ~300 oC and Hg at 160 oC.

The jet chamber could be made from Ti (melt @1668oC) or Niobium (melt @ 2464oC) .As the energy deposited in the windows could be made small, their cooling could be carried by the metal jet itself.

Material for windows are 4Be;  22Ti;  Boron Nitride- BN (5B7N, sublimates @2700oC) and Carbon.

Window could be omitted, but this will require differential pumping and cooled traps.

3.2 Rotating target.

Different types of rotating targets have been discussed in literature for a long time [16]. Due to cyclic nature of motion the volume involved in the process is limited. This type of target could be recommended for power deposition below 10 kW. Examples of beam dump for electrons and photons one can find in [11].

4. FOCUSING

Short, Iron free solenoidal lens is mostly adequate here. Focal distance f of solenoidal lens with longitudinal field at axis  can be found from the following expression

(2)

where  (HR) =pc/300 stands for magnetic rigidity ~33kGxcm for 10MeV particles. For f~2 cm Integral comes to ~66kG2xcm; For contingency ~4cm the field value comes to  4 kG.  For generation of such field the amount of Ampere-turns required goes to be

For the number of turns =10, current in one turn goes to I1~1.3kA.  Conductor cross-section might be ~ 5x10mm2; Cooling carried with de-ionized water. Current density ~26A/mm2, which is ordinary, as the maximal achievable in practice is100 A/mm2.

No flux concentrator is possible for DC; however the current density is different in accordance with the path length difference, so manipulation with thickness of conductor is possible.  Few examples for focusing systems represented below.

4.1 E-166 experiment [13].

Experiment E-166 was dedicated to test an undulator-based positron production scheme [4]. Positron collection system includes DC solenoid with Iron yoke running with current density up to 35A/mm2 delivering focal distance ~4 cm for 10MeV positrons.

4.2 Cornell Positron Source [9].

Modification of the positron source for CESR in 2001 allows for a positron rate ~1011/sec at 50 Hz. Conversion of electrons into positrons is going at 200 MeV.  The focusing coil feed by pulsed current up to 3.5kA with pulse duty at halve height ~20 μs. It is made as partial flux concentrator. Lot of efforts applies for symmetryzation of field pattern around target itself and in focusing coil, taking into account surroundings.

Conversion efficiency with this source ~2.5%,  DC power consumption ~2.5 kW.

5. POSSIBLE SCHEME FOR CEBAF

Possible scheme for CEBAF represented in Fig. 2.

(a)                                                                       (b)

Figure 2.  Possible scheme for CEBAF. (a) Two-layer DC solenoid [15]. (b) Liquid metal target, DC solenoid, adjusting coil followed by triplet.

DC compact solenoid, (a) in Fig.2, cooled by de-ionized water. Triplet (b) serves for matching focusing of compact DC solenoid having azimuthtal symmetry and the rest optics (FODO).

Figure 3.  Addition to the previous scheme is shown here. Al made accelerating structure immersed in solenoid wound with Al conductor.

6. SUMMARY

Polarized positrons could be obtained from polarized electrons in a thin target. The source of ~100mA operating at CEBAF could be used for these purposes. One can expect   efficiency of electron-positron conversion within 0.1% -1%. Power deposited in a target remains below 5 kW for positron current ~1 μA; proportionally lower for lower positron current. Target with liquid metal (Bi-Pb) is mostly adequate here. Collection optics as a DC solenoid recommended for CEBAF positron source.

We recommend a design for 20kW of absorption power as a safe margin; the cost will not be raised much.

# 7. References

1. Olsen, L.C. Maximon, “Photon and Electron Polarization in High-Energy Bremsstrahlung and Pair Production with Screening”,Phys. Rev. 114 (3) (1959 ) 887-904.

2.  H. Bethe, W. Heitler,”On the Stopping of Fast Particles and on the Creation of Positive Electrons”,  Proc. Roy. Soc. A 146 (1934) 83-112.

3. V.E. Balakin and A.A. Mikhailichenko, “The Conversion System for Obtaining High Polarized Electrons and Positrons”, Budker Institute of Nuclear Physics, BINP 79-85 (1979).

4. E.G. Bessonov, “Some Aspects of the Theory and Technology of the Conversion Systems of Linear Colliders”, Proc. 15th Intl. Conf. on High Energy Accel. (Hamburg, 1992), p. 138.

5. E.G. Bessonov, A.A. Mikhailichenko, “A Method of Polarized Positron Beam Production”. June 1996. 3pp., Published  in EPAC96, Barcelona, June 9-14, 1996, Proceedings, p.1516-1518.

6. B. Rossi, “High Energy Particles”, N/Y, 1982.

7. R.Montalbetti, L.Katz, J. Goldemberg, “Photoneutron Cross Sections”, Phys.Rev. 91, 659 (1953).

8. W.P.Swanson, “Calculation of Neutron Yields Released by Electrons Incident on Selected Materials”, Health Physics, Vol.35, pp.353-367, 1978.

9. J. Barley, V. Medjidzade, A. Mikhailichenko, “New Positron Source for CESR”, CBN-01-19, Oct 2001. 16pp.

10. V.A. Tajursky, “Calculation of Electron Conversion into Positrons at 0.2—2GeV”, Budker INP 76-36, Novosibirsk, 1976.

11. A.Mikhailichenko, “Physical Foundations for Design of High Energy Beam Absorbers”, CBN 08-8, Cornell U., LEPP, Ithaca, NY 14853, U.S.A. Available at

http://www.lns.cornell.edu/public/CBN/2008/CBN08-8/CBN08-8.pdf  .

12. D. Yu, M. Lundquist, Y. Luo, A. Smirnov, “Polarized Electron PWT Photoinjectors”, PESP 2008 at Jefferson Lab., DULY Research Inc. California, USA

13. G.Alexander et al, “Observation of Polarized Positrons from an Undulator-Based Source”, SLAC-PUB-13145, DESY-08-025, CLNS-08-2023, COCKCROFT-08-03, DCPT-08-24, IPPP-08-12, Mar 6, 2008. 4pp. Published in Phys.Rev.Lett.100:210801, 2008.

14. A.Mikhailichenko,” ILC Undulator Based Positron Source, Tests and Simulations”, PAC07-WEZAB01, Jun 2007. 5pp. In the Proceedings of Particle Accelerator Conference (PAC 07), Albuquerque, NM, 25-29 Jun 2007, pp 1974-1978.

15. A.Mikhailichenko,” Collection Optics for ILC Positron Target”, PAC07-WEZAB01, Jun 2007. 5pp. In the Proceedings of Particle Accelerator Conference (PAC 07), Albuquerque, New Mexico, 25-29 Jun 2007, pp 1974. Also in *Albuquerque 2007, Particle accelerator* 1974-1978.

http://accelconf.web.cern.ch/AccelConf/p07/PAPERS/WEZAB01.PDF

16. F. Bulos, H. DeStaebler, S. Ecklund, R. Helm, H. Hoag, H. Le Boutet, H. L. Lynch, R. Miller, K. C. Moffeit, “Design of a High Yield Position Source”,  SLAC -PUB – 3635, April 1985. Published in 1985 in IEEE Trans.Nucl.Sci., vol. 32, pp. 1832-1834.

http://slac.stanford.edu/pubs/slacpubs/3500/slac-pub-3635.pdf .

17. H.G Kirk et al , “A High-Power Target Experiment”, Particle Accelerator Conference (PAC2005), Knoxville, TN, Proceedings, pp. 3745-3747.