Positron sources for Linear Colliders

Wei Gai and Wanming Liu

Argonne National Laboratory

9700 S Cass Ave, Argonne, IL, 60439

Abstract.  Positron beams have many applications and there are many different concepts for positron sources.  In this paper, only positron source techniques for linear colliders are covered.   In order to achieve high luminosity, a linear collider positron source for should have a high beam current, high beam energy, small emittance and, for some applications, a high degree of beam polarization.   There are several different schemes presently being developed around the globe. Both the differences between these schemes are presented and their common technical challenges are discussed.

Keywords: Linear collider, Positron source.

PACS:52.59-f,  41.75.Ht

# Introduction

In order to obtain high luminosity in linear colliders, the positron source requirements include a high beam current, high beam energy, and small emittance and possibly high polarization.  High beam energies can be achieved by accelerating the beam in RF linear accelerators and there is not much technical difficulty in accelerating the beam up to TeV.   Small emittances can be achieved using damping rings and there are no major technical difficulties here either.   What remains are the high beam current and polarization requirements.

There are many different positron production schemes.  For linear collider applications positrons are created via the pair production process in a conversion target by 10-30 MeV gamma rays.  The major differences among the different techniques involve how these gamma rays are produced.   Based on the mechanism of gamma production, there exist three major classes of positron sources: conventional, undulator based, and laser Compton based sources.

## Conventional positron source

The conventional positron source is based on bremsstrahlung, the electromagnetic radiation produced by the decceleration of a charged particle, such as an electron, when deflected by another charged particle, such as an atomic nucleus. Typically this process begins by dumping a high energy electron beam into a high-Z target.  If the energy of the bombarding electrons is high enough, the bremsstrahlung is in the gamma ray region of the electromagnetic spectrum.   These gamma rays then interact with nuclei in the same amorphous target and generate positrons via pair production.   The thickness of a conventional positron source target is usually serveral radiation lengths depending on the primary electron beam energy.    Conventional positron sources are usually unpolarized,  but polarized  positrons can be produced using a polarized primary electron beam. In this case pair production and bremsstrahlung are cross-symmetric processes (i.e. the Feynman diagram for electron bremsstrahlung can be obtained from the gamma conversion diagram by flipping the incoming photon and outgoing positron lines) and their cross sections are closely related [1].

Similar to the conventional positron source is another scheme which is based on the channeling effect [2].  The primary electrons experience the collective, screened nuclear fields as if smeared along a string or plane [3, 4] when they are incident on a single crystal at small angles with respect to the crystallographic directions.  For angles of incidence with smaller than the so-called critical angle c [4],  the particle has a low transverse momentum with respect to the axis or plane of the crystal.  Thus it can be restricted to areas away from the nuclei (positively charged particles) or close to the nuclei (negatively charged particles).  In this case the electron is channeled or is guided by the lattice.   As a result of such channeled motion of electrons, channeled electrons emit Kumakhov radiation [5], analogous to the radiation of a magnetic undulator, but with much larger intensity and shorter wavelengths, due to the strength of the Linhard field (~ 102- 103 V/Å,  ~ 3.103 - 3.104 Tesla) and to the short period (~ 1 µm) of the oscillations.    A positron source based the channeling radiation has been proposed by R. Chehab et al. for CLIC and ILC [6].

## Undulator based positron sources

The undulator based positron source was first proposed by V. E. Balakin and A. A. Mikhailichenko [7].  Klaus Flottmann then did a complete study of this idea [1].  Unlike a conventional positron source, the gamma rays in undulator based positron sources are generated as a result of the helical motion of electrons in a periodic magnetic field.   In order to have a sufficiently high  beam current, the primary electron beam energy needs to be >125GeV.  The spectrum of undulator radiation is also a function of the deflection parameter K and and the undulator period u.  The yield of an undulator based positron source varies strongly with the choice of undulator parameter and the electron beam energy [8].   General speaking, lower K will be helpful for the polarization of positron source.  But for a given period length u, lower K also means a lower positron yield.   For a given drive beam energy, a shorter period length u leads to higher positron yields.  But limited by the current technologies, the shortest period achievable is about 1cm with a K maximized around 0.7.   After comparison of several sets of undulator parameters, the ILC RDR baseline positron source undulator was chosen to have K=0.92 and u=1.15cm [9].

## Laser Compton Based Positron Source

For a laser Compton based positron source, the gamma ray is generated through the scattering of a laser photon from a relativistic electron beam.   Electron–photon interactions are mainly governed by two parameters: (i) the density of photons (field strength in classical electrodynamics), and (ii) the energy of each laser photon (frequency in classical electrodynamics).  Analogous to helical undulators, a laser Compton gamma source can be considered as a very short helical undulator with low K and a very short period of several microns.  The advantages of the laser Compton scheme are obvious: (1) high level of positron polarization, (2) independent of the main electron beam, (3) low energy operation.   The disadvantage of a laser Compton based positron source is the lower positron beam intensity. This could be overcome with the additional complication of positron stacking.

Several concepts for an ILC positron source based on Compton scattering have been proposed. They can be categorized into three classes according to the electron source used for the Compton back-scattering. The Linac scheme [10, 11] uses a linac, the Storage Ring scheme [12, 13] employs a storage ring, in which the electron beam circulates many turns and intercepts the laser on each turn. In the ERL (energy recovery linac) scheme [14], electrons are provided by the ERL, a kind of linac topologically equivalent to the storage ring from the energy flow point of view, and the kinetic energy of the spent beam is recovered by its passage through superconducting cavities. As in the linac scheme, the beam property in the ERL is determined by the electron source and the beam transport.   A more detailed comparison of these concepts is available in reference [15]

# Technical Challenges and Possible Solutions

## Rotating target wheel

Shown in Table 1 are the beam parameters of both electrons and positrons at the main linac for different machines.   The ILC has the highest charge per bunch and bunches per pulse. This pulse structure introduces highest dosage of energy deposition in the conversion target compared to the other machines in Table 1.

| TABLE1. Beam parameters of both electrons and positrons at main linac for different machines |
| --- |
|  |  | NLC (1TeV) | CLIC 2008 (0.5 TeV) | CLIC 2008 (3 TeV) | ILC (0.5 TeV) |
| E | GeV | 8 | 9 | 9 | 15 |
| N | 109 | 7.5 | 7 | 3.72-4 | 20 |
| nb |  | 190 | 312 | 312 | 2625 |
| tb | ns | 1.4 | 0.5 | 0.5(6 RF period) | 369 |
| tpulse | ns | 266 | 156 | 156 | 968925 |
| x,y | nm, nm | 3300,30 | 2400,10 | 600,10 | 8400,24 |
| z | m | 90-140 | 72 | 43-45 | 300 |
| E | % | 0.68(3.2%FW) | 2 | 1.5-2 | 1.5 |
| frep | Hz | 120 | 50 | 50 | 5 |
| P | kW | 219 | 180 | 90 | 630 |

Using the beam parameters in Table 1, after sweeping through the parameter space for a conventional positron source, the simple conventional scheme using a W23Re (77% W 23 % Re) target with an AMD (adiabatic matching device) seems not to be viable for ILC due to the excessive energy deposition in the conversion target.

For an undulator based positron source, using an AMD, the energy deposition for the ILC is about 1482J per pulse.  The peak power deposition is about 1.696MW per pulse and the averaged is 7.4KW.  In order for the target to survive, rotating the 2m diameter target wheel at about 1000rpm was estimated to be adequate for safe operation of the target.

Simulations show that rotating the target inside a several Tesla magnetic field is quite challenging.  As shown in figure 2, rotating the ILC target wheel at ~1000rpm will require an additional 650KW of cooling because of eddy current losses.  In order to understand the problem, a prototype target experiment is in progress at the Cockroft institute [16].

FIGURE 1.  Power required for the rotating ILC target in a strong magnetic field

In order to avoid the problem of a rotating target in a high magnetic field, one has to minimize the magnetic field at the target wheel. Several ways to accomplish this have been suggested: one can use a flux concentrator [17], lithium lens [18] or quarter wave transformer.   As there is no technical uncertainty for quarter wave transformer, this option is listed in the ILC RDR as a backup at the cost of a longer undulator length.

For a laser Compton based positron source, since the intensity of each bunch is low, the target doesn’t need to be rotating at high speed and thus rotating the target wheel under a strong magnetic field is not likely to be problematic.

## Liquid metal target

A liquid metal target for the ILC positron source was proposed by A. Mikhailichenko for an undulator based source [19, 20] and adapted by M. Kuriki for the ILC conventional positron source [21].    As presented in [20], the liquid metal target looks promising for the ILC undulator based positron source.   For the ILC conventional positron source, since the energy deposition is much higher in a conventional positron source than in an undulator based source, it is still quite technically challenging even with liquid metal target.  As shown in Figure 2, simulations show that for a conventional positron source using a liquid lead target, the pumping speed needs to be 30m/s in order to prevent the liquid from boiling.

## 300Hz Advanced conventional ILC positron source

In order to solve the problem of excessive power deposition in the target of the ILC conventional positron source, a 300Hz conventional source was proposed by T. Omori.  This 300Hz conventional ILC positron source has a different time structure than the original ILC design, consisting of 5 identical groups of 10 triplets every second.  The length of each group of triplets is about 30ms.  Each triplet is about 952ns long with 3 mini bunch trains of 44 bunches.   Comparing with the original time structure of ILC positron source, this scheme spreads 1320 bunches over 30ms and thus lowers the requirement for pumping speed of the liquid lead target.  As shown in Figure 3, even at a pumping speed of 1m/s, the temperature is still well below the boiling point of liquid lead.

## Channeling based positron source

FIGURE 4.  Schematic of a positron source based on the channeling effect.

As sketched in Figure 4, a multi GeV electron beam striking a crystal will generate high intensity gamma rays and some positrons.  Using a bending magnet to bend electrons and positrons away, only the gamma rays are used to strike an amorphous target to generate positrons via the pair production process.  This scheme could lower the energy deposition in the target to the same level as an undulator based positron source and thus avoid the complications of targeting for conventional positron sources.

# Summary

Positron source concepts for linear colliders are reviewed.  The differences between these schemes are presented and their common technical challenges are discussed.

For a conventional ILC positron source, the energy deposition in the target is so high that solid metal target will not survive.  A 300 Hz advanced conventional positron source employing a liquid lead target could possibly solve this problem.  Another solution would be the use of a channeling based source which should have an energy deposition level comparable to an undulator based positron source.

Undulator based positron sources have difficulties related to the use of a rotating target inside a strong magnetic field.  This could be overcome at the cost of a longer undulator length by using a quarter wave transformer instead of an AMD.  Other options include using a lithium lens and a flux concentrator.  A flux concentrator can reduce the magnetic field at the target at the cost of a slightly lower capture efficiency.  Research on prototyping a flux concentrator suitable for ILC is ongoing at LLNL.  Lithium lenses have good capture efficiencies and develop in theory a low magnetic field on the target.  Studies on its viability are needed and are in progress at Cornell.

For a laser Compton based positron source,  its per bunch intensity is low and thus it won’t have the problems of the other two schemes.  It requires, however, an additional storage ring for positron stacking.

# References

[1] Flöttmann, K. 1993, “Investigation toward the development of polarized and unpolarized high intensity positron sources for linear collider”,  DESY 93-161

[2] R. Chehab et al. Study of a Positron Source Generated by Photons from Ultrarelativistic Channeled Particles, Proceedings of the 1989 IEEE Particle Accelerator Conference. 20-23 Mar 1989, Chicago, Illinois 13th IEEE Particle Accelerator Conference., p.283

[3] Lindhard, J., 1965, “Influence of crystal lattice on motion of energetic charged particles,” K. Dan. Vidensk. Selsk. Mat. Fys. Medd. 34 (14), 1–64.

[4] Ulrik I. Uggerhøj, 2005,  “The interaction of relativistic particles with strong crystalline fields”, Rev. Mod. Phys., 77(4) 1131-1171

[5] M.A. Kumakhov, Physics Letters A57 (1976) 17

[6]  R. Chehab et al.  A Positron Source Using Channeling in Crystals for Linear Colliders, Channeling2008, Erice,  Oct.2008

[7] V.E. Balakin, A. A. Mikhailichenko,  1979, The Conversion system for obtaining high polarized electrons and positrons, INP 79-85

[8] W. Liu, W. Gai and K-J Kim, Systematic Study of The Undulator based ILC Positron Source: Production and Capture, Proceedings of PAC07, Albuquerque, New Mexico, USA

[9] ILC Reference Design Report (RDR), (August 2007)

[10] T. Omori et al., Design of a polarized positron source for linear colliders, NIM A (500), pp232-252 (November 2002)

[11] V. Yakimenko and I. Pogorelsky, Polarized y source based on Compton backscattering in a laser cavity, Pys. Rev. ST Accel. Beams 9, 091001 (2006)

[12] S. Araki et al., KEK-Preprint2005-60, CLIC Note 639 (2005).

[13] F. Zimmermann, et al., CLIC Polarized Positron Source Based on Laser Compton Sscattering, Proc. EPAC06, Edinburgh (June 2006)

[14] T. Omori, ERL based Compton scheme, Proc. of Posipol07, Paris (May 2007)

[15]  M. Kuriki, et al, ILC Positron Source Based on Laser Compton, Polarized Ion Sources, Targets and Polarimetry-PSTP 2007.

[16] I. R. Bailey, et al, A Prototype Target Wheel for The ILC Positron Source, Proceedings of EPAC08, Genoa, Italy

[17] H. Brechna, D. A. Hill and B. M. Bally, “150 kOe Liquid Nitrogen Cooled Flux-Concentrator Magnet”, Rev. Sci. Instr., 36 1529, 1965

[18] A.Mikhailichenko, Lithium Lens for Positron Production System, CBN 08-5

[19] A.Mikhailichenko, “Positron Source for ILC. A Perspective”, CBN06-1, Cornell, 2006

[20] A.Mikhailichenko,  Liquid Metal Target for ILC, Proceedings of EPAC 2006, Edinburgh, Scotland

[21] M. Kuriki, ILC Positron Source Based on Liquid Metal Target, Proceedings of the4th Annual Meeting of Particle Accelerator Society of Japan and the 32nd Linear Accelerator Meeting in Japan (August 1-3, 2007, Wako Japan)

# Text boxes

FIGURE 2.  Temperature evolution of liquid lead target for ILC conventional positron source

FIGURE 3.  Temperature distribution in liquid lead target after 10 triplets